## Slide 1: OPENOCD Porting Guide
VERTEXCOM © 2020
DARKO PANCEV

## Slide 2
Important Porting Files
contrib
loaders
flash
vcm4x_word_program.s
vcm4x_page_program.s
src
flash
nor
vcm4.c
src
flash
nor
drivers.c
tcl
board
vertexcom-vcm4.cfg
src
flash
nor
Makefile.am
tcl
target
vcm4.cfg

## Slide 3
How to build OpenOCD image?
Move to root directory of OpenOCD
Run ./configure
After finish run ‘make clean && make’
OpenOCD image will be in ‘src’ directory as openocd
To test the openocd image whether it build successfully or not, run ‘./src/openocd -v’ to see the openocd version like this:
How to flash new image with openocd using SWD interface?
Copy your binary file to ‘tcl’ directory.
Move to ‘tcl’ directory.
From ‘tcl’ director run:
../src/openocd -f board/vertexcom-cm4.cfg -c “program your_image.bin reset exit 0”

## Slide 4
tcl/board/vertexcom-vcm4.cfg
source [find interface/jlink.cfg]
transport select swd
source [find target/vcm4.cfg]

## Slide 5
tcl/target/vcm4.cfg
source [find target/swj-dp.tcl]
if { [info exist CHIPNAME] } {
set _CHIPNAME $CHIPNAME
} else {
set _CHIPNAME vcm4
}
if { [info exists ENDIAN] } {
set _ENDIAN $ENDIAN
} else {
set _ENDIAN little
}
# Work-area is a space in RAM used for flash programming
# By default use 16kB
if { [info exists WORKAREASIZE] } {
set _WORKAREASIZE $WORKAREASIZE
} else {
set _WORKAREASIZE 0x10000
}
if { [info exists CPUTAPID] } {
set _CPUTAPID $CPUTAPID
} else {
set _CPUTAPID 0x2ba01477
}
adapter_khz 1000
swj_newdap $_CHIPNAME cpu -expected-id $_CPUTAPID
set _TARGETNAME $_CHIPNAME.cpu
target create $_TARGETNAME cortex_m -endian $_ENDIAN -chain-position $_TARGETNAME
$_TARGETNAME configure -work-area-phys 0x20000000 -work-area-size $_WORKAREASIZE -work-area-backup 0
set _FLASHNAME $_CHIPNAME.flash
flash bank $_FLASHNAME vcm4 0x00000000 0 0 0 $_TARGETNAME
reset_config none separate

## Slide 6
tcl/target/vcm4.cfg
proc vcm4_default_examine_end {} {
# disable watchdog timer
mww 0x40048040 0xaa5555aa
mww 0x40048044 0x00000000
}
proc vcm4_default_reset_start {} {
# after reset the clock run at 6 MHz
#adapter_khz 1000
}
proc vcm4_default_reset_init {} {
# configure the clock to run at 150 MHz
#mww 0x4004b004 0x0000ba52
#mww 0x4004b008 0x05800000
#sleep 10
#mww 0x40047004 0x00000002
#sleep 10
# boost JTAG frequency
# adapter_khz 6000
}
# default hooks
$_TARGETNAME configure -event examine-end { vcm4_default_examine_end }
$_TARGETNAME configure -event reset-start { vcm4_default_reset_start }
$_TARGETNAME configure -event reset-init { vcm4_default_reset_init }

## Slide 7
src/flash/nor/vcm4.c
#ifdef HAVE_CONFIG_H
#include "config.h"
#endif
#include "imp.h"
#include <target/algorithm.h>
#include <target/armv7m.h>
#include <helper/types.h>
#define VCM4_VERSION_ID 0x4004803C
/* vcm4 flash csr register */
enum vcm4_fcsr_registers {
FCSR_BASE = 0x40020000,
#define FCSR_REG(offset) (FCSR_BASE + offset)
FCSR_FLASH_CMD = FCSR_REG(0x000), // flash controller command register
FCSR_FLASH_ADDR = FCSR_REG(0x004), // flash controller address regsiter
FCSR_FLASH_CFG = FCSR_REG(0x008), // flash controller configuration register
FCSR_FLASH_CACHE = FCSR_REG(0x00C), // flash controller cache configuration register
FCSR_FLASH_SR = FCSR_REG(0x010), // flash controller SPI flash status register
FCSR_FLASH_ID = FCSR_REG(0x014), // flash controller SPI flash ID register
FCSR_FLASH_CACHEHIT = FCSR_REG(0x018), // cache hit rate counting register
FCSR_FLASH_INVADDR_S = FCSR_REG(0x020), // invalid/flush cache start address
FCSR_FLASH_INVADDR_E = FCSR_REG(0x024), // invalid/flush cache end address
FCSR_FLASH_CACHE_INV = FCSR_REG(0x028), // invalid cache control register
FCSR_FLASH_CACHE_FLUSH = FCSR_REG(0x02C), // flush cache control register
FCSR_FLASH_BUF0 = FCSR_REG(0x100), // flash controller read/write buffer 0
FCSR_FLASH_BUF63 = FCSR_REG(0x1FC), // flash controller read/write buffer 63
};
/* vcm4 flash bit-fields */
#define FLASH_CMD_ACT_Pos (31)
#define FLASH_CMD_ACT_Msk (0x1 << FLASH_CMD_ACT_Pos)
#define FLASH_CMD_POLL_Pos (24)
#define FLASH_CMD_POLL_Msk (0x1 << FLASH_CMD_POLL_Pos)
#define FLASH_CMD_LENGTH_Pos (16)
#define FLASH_CMD_LENGTH_Msk (0xFF << FLASH_CMD_LENGTH_Pos)
#define FLASH_CMD_CMDMODE_Pos (12)
#define FLASH_CMD_CMDMODE_Msk (0x7 << FLASH_CMD_CMDMODE_Pos)
#define FLASH_CMD_CMDADDR4_Pos (11)
#define FLASH_CMD_CMDADDR4_Msk (0x1 << FLASH_CMD_CMDADDR4_Pos)
#define FLASH_CMD_CMDADDR_Pos (10)
#define FLASH_CMD_CMDADDR_Msk (0x1 << FLASH_CMD_CMDADDR_Pos)
#define FLASH_CMD_CMDWR_Pos (9)
#define FLASH_CMD_CMDWR_Msk (0x1 << FLASH_CMD_CMDWR_Pos)
#define FLASH_CMD_CMDDATA_Pos (8)
#define FLASH_CMD_CMDDATA_Msk (0x1 << FLASH_CMD_CMDDATA_Pos)
#define FLASH_CMD_CMDID_Pos (0)
#define FLASH_CMD_CMDID_Msk (0xFF << FLASH_CMD_CMDID_Pos)

## Slide 8
src/flash/nor/vcm4.c
#define WINBOND_CMDID_WRSR1 0x01 // write status register 1
#define WINBOND_CMDID_WRSR2 0x31 // write status register 2
#define WINBOND_CMDID_RDSR1 0x05 // read status register 1
#define WINBOND_CMDID_RDSR2 0x35 // read status register 2
#define WINBOND_CMDID_PAGE_PROG 0x02 // page program
#define WINBOND_CMDID_READ_DATA 0x03 // read data
#define WINBOND_CMDID_WRITE_DISABLE 0x04 // write disable
#define WINBOND_CMDID_WRITE_ENABLE 0x06 // write enable
#define WINBOND_CMDID_FAST_READ 0x0B // fast read
#define WINBOND_CMDID_RDCR 0x15 // read configuration register
#define WINBOND_CMDID_SECTOR_ERASE 0x20 // sector erase
#define WINBOND_CMDID_QUADPAGE_PROG 0x32 // quad page program
#define WINBOND_CMDID_BLOCK_ERASE_32K 0x52 // 32K block erase
#define WINBOND_CMDID_BLOCK_ERASE_64K 0xD8 // 64K block erase
#define WINBOND_CMDID_CHIP_ERASE 0xC7 // chip erase
#define WINBOND_MF 0xEF
struct vcm4_info {
uint32_t code_page_size;
bool probed;
struct target *target;
};
struct vcm4_device_spec {
uint32_t version_id;
const char *variant;
uint8_t sector_size_kb;
unsigned int flash_size_kb;
};
static const struct vcm4_device_spec vcm4_known_device_table[] = {
{
.version_id = 0x19061001,
.variant = "phoenix",
.sector_size_kb = 4,
.flash_size_kb = 2048,
},
};

## Slide 9
src/flash/nor/vcm4.c
static int vcm4_flash_write_enable(struct vcm4_info *chip)
{
int res = ERROR_OK;
uint32_t temp = 0;
temp |= (1 << FLASH_CMD_ACT_Pos);
temp |= (WINBOND_CMDID_WRITE_ENABLE << FLASH_CMD_CMDID_Pos);
res = target_write_u32(chip->target, FCSR_FLASH_CMD, temp);
res = vcm4_flash_wait_for_action_done(chip, 100);
return res;
}
static int vcm4_flash_program_word(struct vcm4_info *chip, uint32_t addr, uint32_t data)
{
int res = ERROR_OK;
uint32_t temp = 0;
res = vcm4_flash_write_enable(chip);
if (res != ERROR_OK) {
return res;
}
temp |= (1 << FLASH_CMD_ACT_Pos);
temp |= (1 << FLASH_CMD_CMDADDR_Pos);
temp |= (1 << FLASH_CMD_CMDWR_Pos);
temp |= (1 << FLASH_CMD_CMDDATA_Pos);
temp |= (3 << FLASH_CMD_LENGTH_Pos); // 1 word (4 bytes) - 1
temp |= (WINBOND_CMDID_PAGE_PROG << FLASH_CMD_CMDID_Pos);
res = target_write_u32(chip->target, FCSR_FLASH_BUF0, data);
if (res != ERROR_OK) {
return res;
}
res = target_write_u32(chip->target, FCSR_FLASH_ADDR, addr);
if (res != ERROR_OK) {
return res;
}
res = target_write_u32(chip->target, FCSR_FLASH_CMD, temp);
if (res != ERROR_OK) {
return res;
}
res = vcm4_flash_wait_for_action_done(chip, 100);
return res;
}

## Slide 10
src/flash/nor/vcm4.c
static int vcm4_flash_program_page(struct vcm4_info *chip, uint32_t addr, uint32_t bytes, uint8_t *buf)
{
int res = ERROR_OK;
uint32_t i = 0;
uint32_t temp = 0;
uint32_t data;
res = vcm4_flash_write_enable(chip);
if (res != ERROR_OK) {
return res;
}
for (i = 0; i < bytes; i += 4) {
memcpy(&data, &buf[i], sizeof(uint32_t));
res = target_write_u32(chip->target, FCSR_FLASH_BUF0 + i, data);
if (res != ERROR_OK) {
return res;
}
}
temp |= (1 << FLASH_CMD_ACT_Pos);
temp |= (1 << FLASH_CMD_CMDADDR_Pos);
temp |= (1 << FLASH_CMD_CMDWR_Pos);
temp |= (1 << FLASH_CMD_CMDDATA_Pos);
temp |= ((bytes - 1) << FLASH_CMD_LENGTH_Pos);
temp |= (WINBOND_CMDID_PAGE_PROG << FLASH_CMD_CMDID_Pos);
res = target_write_u32(chip->target, FCSR_FLASH_ADDR, addr);
if (res != ERROR_OK) {
return res;
}
res = target_write_u32(chip->target, FCSR_FLASH_CMD, temp);
if (res != ERROR_OK) {
return res;
}
res = vcm4_flash_wait_for_action_done(chip, 1000);
return res;
}

## Slide 11
src/flash/nor/vcm4.c
static int vcm4_flash_write(struct vcm4_info *chip, uint32_t offset, const uint8_t *buffer, uint32_t bytes)
{
struct target *target = chip->target;
uint32_t buffer_size = 16384;
struct working_area *write_algorithm;
struct working_area *source;
uint32_t address = offset;
struct reg_param reg_params[5];
struct armv7m_algorithm armv7m_info;
int res = ERROR_OK;
LOG_INFO("writing buffer to flash offset=0x%"PRIx32" bytes=0x%"PRIx32, offset, bytes);
assert(bytes % 4 == 0);
/* allocate working area with flash programming code */
if (target_alloc_working_area(target, sizeof(vcm4_flash_write_code), &write_algorithm) != ERROR_OK) {
LOG_INFO("can't allocate working area for write algorithm use slow mode!");
for (uint32_t i = 0; i < bytes; i += 256) {
res = vcm4_flash_program_page(chip, offset, 256, (uint8_t *)buffer);
offset += 256;
buffer += 256;
}
return ERROR_OK;
}
res = target_write_buffer(target, write_algorithm->address,
sizeof(vcm4_flash_write_code),
vcm4_flash_write_code);
if (res != ERROR_OK) {
return res;
}
/* memory buffer */
while (target_alloc_working_area(target, buffer_size, &source) != ERROR_OK) {
buffer_size /= 2;
if (buffer_size <= 256) {
/* free working area, write algorithm already allocated */
target_free_working_area(target, write_algorithm);
LOG_WARNING("No large enough working area available, can't do block memory writes");
return ERROR_TARGET_RESOURCE_NOT_AVAILABLE;
}
}
armv7m_info.common_magic = ARMV7M_COMMON_MAGIC;
armv7m_info.core_mode = ARM_MODE_THREAD;
init_reg_param(&reg_params[0], "r0", 32, PARAM_IN_OUT); /* buffer start, status (out) */
init_reg_param(&reg_params[1], "r1", 32, PARAM_OUT); /* buffer end */
init_reg_param(&reg_params[2], "r2", 32, PARAM_OUT); /* flash target address */
init_reg_param(&reg_params[3], "r3", 32, PARAM_OUT); /* bytes */
init_reg_param(&reg_params[4], "r4", 32, PARAM_OUT); /* flash base */
buf_set_u32(reg_params[0].value, 0, 32, source->address);
buf_set_u32(reg_params[1].value, 0, 32, source->address + source->size);
buf_set_u32(reg_params[2].value, 0, 32, address);
buf_set_u32(reg_params[3].value, 0, 32, bytes);
buf_set_u32(reg_params[4].value, 0, 32, FCSR_BASE);

## Slide 12
src/flash/nor/vcm4.c
res = target_run_flash_async_algorithm(target, buffer, bytes/4, 4,
0, NULL,
5, reg_params,
source->address, source->size,
write_algorithm->address, 0,
&armv7m_info);
if (res == ERROR_FLASH_OPERATION_FAILED) {
LOG_ERROR("error executing vcm3 flash write algorithm");
res = ERROR_FAIL;
}
target_free_working_area(target, source);
target_free_working_area(target, write_algorithm);
destroy_reg_param(&reg_params[0]);
destroy_reg_param(&reg_params[1]);
destroy_reg_param(&reg_params[2]);
destroy_reg_param(&reg_params[3]);
destroy_reg_param(&reg_params[4]);
return res;
}

## Slide 13
contrib/loaders/flash/vcm4x_word_program.s
/*
* Params :
* r0 = workarea start
* r1 = workarea end
* r2 = flash address
* r3 = byte count
* r4 = flash base [0x40020000]
*
* r6 - temp
* r7 - rp
* r8 - wp, tmp
*/
#define FCSR_FLASH_CMD_OFFSET 0x000
#define FCSR_FLASH_ADDR_OFFSET 0x004
#define FCSR_FLASH_BUF0_OFFSET 0x100
wait_fifo:
ldr r8, [r0, #0] /* read wp */
cmp r8, #0 /* abort if wp == 0 */
beq exit
ldr r7, [r0, #4] /* read rp */
cmp r7, r8 /* wait until rp != wp */
beq wait_fifo
ldr r6, FLASH_WRITE_ENABLE /* write enable */
str r6, [r4, #FCSR_FLASH_CMD_OFFSET]
wait_write_enable:
ldr r6, [r4, #FCSR_FLASH_CMD_OFFSET] /* load CMD register */
tst r6, #0x80000000 /* ACT (bit31) == 1 => operation in progress */
bne wait_write_enable /* wait more ... */
ldr r6, [r7], #0x4 /* read one word from src, increment ptr */
str r6, [r4, #FCSR_FLASH_BUF0_OFFSET]
mov r6, r2
adds r2, #0x4 /* increment the addres */
str r6, [r4, #FCSR_FLASH_ADDR_OFFSET]
ldr r6, FLASH_WORD_PROGRAM
str r6, [r4, #FCSR_FLASH_CMD_OFFSET]
wait_write_program:
ldr r6, [r4, #FCSR_FLASH_CMD_OFFSET] /* load CMD register */
tst r6, #0x80000000 /* ACT (bit31) == 1 => operation in progress */
bne wait_write_program /* wait more ... */
cmp r7, r1 /* wrap rp at end of buffer */
bcc no_wrap
mov r7, r0
adds r7, #8 /* skip loader args */
no_wrap:
str r7, [r0, #4] /* store rp */
subs r3, #4 /* decrement byte count */
bne wait_fifo
exit:
bkpt #0x00
FLASH_WRITE_ENABLE: .word 0x81000006
FLASH_WORD_PROGRAM: .word 0x81030702

## Slide 14
contrib/loaders/flash/vcm4x_word_program.s
arm-none-eabi-gcc -c vcm4x_word_program.s
arm-none-eabi-objdump -d vcm4x_word_program.o
vcm4x_word_program.o: file format elf32-littlearm
Disassembly of section .text:
00000000 <wait_fifo>:
0: f8d0 8000 ldr.w r8, [r0]
4: f1b8 0f00 cmp.w r8, #0
8: d01d beq.n 46 <exit>
a: 6847 ldr r7, [r0, #4]
c: 4547 cmp r7, r8
e: d0f7 beq.n 0 <wait_fifo>
10: f8df 6034 ldr.w r6, [pc, #52] ; 48 <FLASH_WRITE_ENABLE>
14: 6026 str r6, [r4, #0]
00000016 <wait_write_enable>:
16: 6826 ldr r6, [r4, #0]
18: f016 4f00 tst.w r6, #2147483648 ; 0x80000000
1c: d1fb bne.n 16 <wait_write_enable>
1e: f857 6b04 ldr.w r6, [r7], #4
22: f8c4 6100 str.w r6, [r4, #256] ; 0x100
26: 4616 mov r6, r2
28: 3204 adds r2, #4
2a: 6066 str r6, [r4, #4]
2c: 4e07 ldr r6, [pc, #28] ; (4c <FLASH_WORD_PROGRAM>)
2e: 6026 str r6, [r4, #0]
00000030 <wait_write_program>:
30: 6826 ldr r6, [r4, #0]
32: f016 4f00 tst.w r6, #2147483648 ; 0x80000000
36: d1fb bne.n 30 <wait_write_program>
38: 428f cmp r7, r1
3a: d301 bcc.n 40 <no_wrap>
3c: 4607 mov r7, r0
3e: 3708 adds r7, #8
00000040 <no_wrap>:
40: 6047 str r7, [r0, #4]
42: 3b04 subs r3, #4
44: d1dc bne.n 0 <wait_fifo>
00000046 <exit>:
46: be00 bkpt 0x0000
00000048 <FLASH_WRITE_ENABLE>:
48: 81000006 .word 0x81000006
0000004c <FLASH_WORD_PROGRAM>:
4c: 81030702 .word 0x81030702
static const uint8_t vcm4_flash_write_code[] = {
/* see contrib/loaders/flash/vcm4x_word_program.S */
0xd0, 0xf8, 0x00, 0x80,
0xb8, 0xf1, 0x00, 0x0f,
0x1c, 0xd0,
0x47, 0x68,
0x47, 0x45,
0xf7, 0xd0,
0xdf, 0xf8, 0x34, 0x60,
0x26, 0x60,
0x26, 0x68,
0x16, 0xf0, 0x00, 0x4f,
0xfb, 0xd1,
0x57, 0xf8, 0x04, 0x6b,
0xc4, 0xf8, 0x00, 0x61,
0x16, 0x46,
0x04, 0x32,
0x66, 0x60,
0x07, 0x4e,
0x26, 0x60,
0x26, 0x68,
0x16, 0xf0, 0x00, 0x4f,
0xfb, 0xd1,
0x8f, 0x42,
0x01, 0xd3,
0x07, 0x46,
0x08, 0x37,
0x47, 0x60,
0x04, 0x3b,
0xdc, 0xd1,
0x00, 0xbe,
0x06, 0x00, 0x00, 0x81,
0x02, 0x07, 0x03, 0x81,
};

## Slide 15
contrib/loaders/flash/vcm4x_page_program.s
/*
* Params :
* r0 = workarea start
* r1 = workarea end
* r2 = flash address
* r3 = byte count
* r4 = flash base [0x40020000]
*
* r5 - flash buffer, r6 - temp, r7 - rp, r8 - wp, tmp
*/
#define FCSR_FLASH_CMD_OFFSET 0x000
#define FCSR_FLASH_ADDR_OFFSET 0x004
ldr r5, FLASH_BUF_START_ADDR
wait_fifo:
ldr r8, [r0, #0] /* read wp */
cmp r8, #0 /* abort if wp == 0 */
beq exit
ldr r7, [r0, #4] /* read rp */
cmp r7, r8 /* wait until rp != wp */
beq wait_fifo
ldr r8, FLASH_BUF_END_ADDR
cmp r5, r8
blt fill_flash_buf /* jump to fill_flash_buf in case r8 is bigger */
ldr r6, FLASH_WRITE_ENABLE
str r6, [r4, #FCSR_FLASH_CMD_OFFSET]
wait_write_enable:
ldr r6, [r4, #FCSR_FLASH_CMD_OFFSET]
tst r6, #0x80000000
bne wait_write_enable
ldr r6, [r7], #0x4 /* read one word from src, increment ptr */
str r6, [r5], #0x4 /* store one word to flash buffer, and increment flash buf */
mov r6, r2
adds r2, #0x100
str r6, [r4, #FCSR_FLASH_ADDR_OFFSET]
ldr r6, FLASH_PAGE_PROGRAM
str r6, [r4, #FCSR_FLASH_CMD_OFFSET]
wait_write_program:
ldr r6, [r4, #FCSR_FLASH_CMD_OFFSET]
tst r6, #0x80000000
bne wait_write_program
ldr r5, FLASH_BUF_START_ADDR
b wrap_rp_at_end_of_buffer
fill_flash_buf:
ldr r6, [r7], #0x4 /* read one word from src, increment ptr */
str r6, [r5], #0x4 /* store one word to flash buffer, and increment flash buf */
wrap_rp_at_end_of_buffer:
cmp r7, r1 /* wrap rp at end of buffer */
bcc no_wrap
mov r7, r0
adds r7, #8 /* skip loader args */
no_wrap:
str r7, [r0, #4] /* store rp */
subs r3, #4 /* decrement byte count */
bne wait_fifo
exit:
bkpt #0x00
FLASH_BUF_START_ADDR: .word 0x40020100
FLASH_BUF_END_ADDR: .word 0x400201fc
FLASH_WRITE_ENABLE: .word 0x81000006
FLASH_PAGE_PROGRAM: .word 0x81ff0702

## Slide 16
contrib/loaders/flash/vcm4x_page_program.s
vcm4x_page_program.o: file format elf32-littlearm
Disassembly of section .text:
00000000 <wait_fifo-0x2>:
0: 4d17 ldr r5, [pc, #92] ; (60 <FLASH_BUF_START_ADDR>)
00000002 <wait_fifo>:
2: f8d0 8000 ldr.w r8, [r0]
6: f1b8 0f00 cmp.w r8, #0
a: d028 beq.n 5e <exit>
c: 6847 ldr r7, [r0, #4]
e: 4547 cmp r7, r8
10: d0f7 beq.n 2 <wait_fifo>
12: f8df 8050 ldr.w r8, [pc, #80] ; 64 <FLASH_BUF_END_ADDR>
16: 4545 cmp r5, r8
18: db16 blt.n 48 <fill_flash_buf>
1a: 4e13 ldr r6, [pc, #76] ; (68 <FLASH_WRITE_ENABLE>)
1c: 6026 str r6, [r4, #0]
0000001e <wait_write_enable>:
1e: 6826 ldr r6, [r4, #0]
20: f016 4f00 tst.w r6, #2147483648 ; 0x80000000
24: d1fb bne.n 1e <wait_write_enable>
26: f857 6b04 ldr.w r6, [r7], #4
2a: f845 6b04 str.w r6, [r5], #4
2e: 4616 mov r6, r2
30: f512 7280 adds.w r2, r2, #256 ; 0x100
34: 6066 str r6, [r4, #4]
36: 4e0d ldr r6, [pc, #52] ; (6c <FLASH_PAGE_PROGRAM>)
38: 6026 str r6, [r4, #0]
0000003a <wait_write_program>:
3a: 6826 ldr r6, [r4, #0]
3c: f016 4f00 tst.w r6, #2147483648 ; 0x80000000
40: d1fb bne.n 3a <wait_write_program>
42: f8df 501c ldr.w r5, [pc, #28] ; 60 <FLASH_BUF_START_ADDR>
46: e003 b.n 50 <wrap_rp_at_end_of_buffer>
00000048 <fill_flash_buf>:
48: f857 6b04 ldr.w r6, [r7], #4
4c: f845 6b04 str.w r6, [r5], #4
00000050 <wrap_rp_at_end_of_buffer>:
50: 428f cmp r7, r1
52: d301 bcc.n 58 <no_wrap>
54: 4607 mov r7, r0
56: 3708 adds r7, #8
00000058 <no_wrap>:
58: 6047 str r7, [r0, #4]
5a: 3b04 subs r3, #4
5c: d1d1 bne.n 2 <wait_fifo>
0000005e <exit>:
5e: be00 bkpt 0x0000
00000060 <FLASH_BUF_START_ADDR>:
60: 40020100 .word 0x40020100
00000064 <FLASH_BUF_END_ADDR>:
64: 400201fc .word 0x400201fc
00000068 <FLASH_WRITE_ENABLE>:
68: 81000006 .word 0x81000006
0000006c <FLASH_PAGE_PROGRAM>:
6c: 81ff0702 .word 0x81ff0702
static const uint8_t vcm4_flash_write_code[] = {
/* see contrib/loaders/flash/vcm4x_page_program.S */
0x17, 0x4d,
0xd0, 0xf8, 0x00, 0x80,
0xb8, 0xf1, 0x00, 0x0f,
0x28, 0xd0,
0x47, 0x68,
0x47, 0x45,
0xf7, 0xd0,
0xdf, 0xf8, 0x50, 0x80,
0x45, 0x45,
0x16, 0xdb,
0x13, 0x4e,
0x26, 0x60,
0x26, 0x68,
0x16, 0xf0, 0x00, 0x4f,
0xfb, 0xd1,
0x57, 0xf8, 0x04, 0x6b,
0x45, 0xf8, 0x04, 0x6b,
0x16, 0x46,
0x12, 0xf5, 0x80, 0x72,
0x66, 0x60,
0x0d, 0x4e,
0x26, 0x60,
0x26, 0x68,
0x16, 0xf0, 0x00, 0x4f,
0xfb, 0xd1,
0xdf, 0xf8, 0x1c, 0x50,
0x03, 0xe0,
0x57, 0xf8, 0x04, 0x6b,
0x45, 0xf8, 0x04, 0x6b,
0x8f, 0x42,
0x01, 0xd3,
0x07, 0x46,
0x08, 0x37,
0x47, 0x60,
0x04, 0x3b,
0xd1, 0xd1,
0x00, 0xbe,
0x00, 0x01, 0x02, 0x40,
0xfc, 0x01, 0x02, 0x40,
0x06, 0x00, 0x00, 0x81,
0x02, 0x07, 0xff, 0x81,
};

## Slide 17
Phoenix and Sirius Performance Comparison
 | SIRIUS (VC7300) | PHOENIX (VC6320)
MCU Clock Speed | 39.3216 MHz | 150 MHz
Adapter KHz (Interface Speed) | 1000 KHz | 8000 KHz
Test Image Size | ~250 KB (WISUN) | ~280 KB (G3PLC)
FLASH IP | Embedded Flash | SPI Flash
FastMode programming block size allocated in RAM | 16 KB | 32 KB
SlowMode WORD PROGRAM | ~10 Seconds | ~130 Seconds
SlowMode PAGE PROGRAM | - | ~38 Seconds
FastMode WORD PROGRAM | ~3 Seconds | ~9 Seconds
FastMode PAGE PROGRAM | - | ~9 Seconds